3-Part CSI MasterFormat Specification

SECTION 10 2600

WALL AND DOOR PROTECTION

- GENERAL

## SECTION INCLUDES

### 2 inch (50.8mm) by 2 inch (50.8mm) Corner Guard, Recess Mount, Fire Barrier 2HR

### 2 inch (50.8mm) by 2 inch (50.8mm) Corner Guard, Recess Mount, End Wall, Fire Barrier 2HR

## SUBMITTALS

### Comply with requirements of Section 01 33 00 Submittals.

### Product data: Submit manufacturer’s product data.

### Shop drawing: Submit shop drawings showing components, dimensions, anchorage details.

### Samples: Submit for approval 12 inch (304.8mm) long sample for each model and color specified, including end caps and corner units.

### Test reports: Submit manufacturer’s test reports and certification indicating compliance with applicable ADA and building code requirements

  - QUALITY ASSURANCE

    - Comply with NFPA 101 for interior finish materials. Smoke developed less than 450 degree F and flame spread of 25 or less in accordance with ASTM E84.

  - DELIVERY, STORAGE AND HANDLING

### Delivery: Deliver materials to site in manufacturer’s original, unopened containers and packaging with labels clearly indicating manufacturer and material.

### Storage: Store materials indoors in a clean, dry area protected from damage and in accordance with manufacturer’s instructions.

### Handling: Protect materials during handling and installation to prevent damage

- PRODUCTS

2.01 	MANUFACTURER

Nystrom

9300 73rd Ave N

Minneapolis, MN 55428

PH: 800.547.2635

www.Nystrom.com

2.02 	CORNER GUARD, Vinyl, 2 inch, Recess Mount, Fire Barrier 2HR

- Nystrom model CGVF2S corner guard with fire barrier 2 hour mounted on continuous aluminum retainer. Exposed surfaces shall be free of wrinkling, chipping, discoloration, or other imperfections.

  - Dimensions

    - Wing size: 2 inch (50.8mm)

    - Corner angle type: 90 degree standard 1/4 inch radius

  - Profile: High impact vinyl acrylic extrusion locked into place, nominal 0.078 inch (1.98mm) thick. Class A fire rating, tested in accordance with ASTM E 84.

  - Extrusion: Pebble grain finish. Contains EPA registered Micro-Chek antimicrobial agent.

  - Retainer: Continuous 6063-T5 aluminum retainer, nominal 0.060 inch (1.52mm) thick.

  - Base: 4 inch (101.3mm) high 6063-T5 aluminum base pre-attached to aluminum retainer.

  - Color: To be selected from manufacture’s standard colors.

2.03 	CORNER GUARD, Vinyl, 2 inch, Recess Mount, End Wall, Fire Barrier 2HR

- Nystrom model CGVF2S-EW4875 End Wall corner guard with fire barrier 2 hour assembly composed of two (2) recess mounted corner guards with 2 inch wings mounted over continuous aluminum retainer with a filler spacer. Exposed surfaces shall be free of wrinkling, chipping, discoloration, or other imperfections.

  - Dimensions

    - Wing size: 2 inch (50.8mm)

    - Corner angles: 90 degree standard 1/4 inch radius

  - Profile: High impact vinyl acrylic extrusion locked into place, nominal 0.078 inch (1.98mm) thick. Class A fire rating, tested in accordance with ASTM E 84.

  - Extrusion: Pebble grain finish. Contains EPA registered Micro-Chek antimicrobial agent.

  - Retainer: Continuous 6063-T5 aluminum retainer, nominal 0.062 inch (1.57mm) thick.

  - Base: 4 inch (101.3mm) high 6063-T5 aluminum base pre-attached to aluminum retainer

  - Color: To be selected from manufacture’s standard colors.

  - Spacer sheet: Variable width high impact filler sheet in the same color and texture to that of the corner guards.

- EXECUTION

3.01 EXAMINATION

- Verify by examination that wall surface is acceptable to receive the specified bumper guard. Notify the Architect in writing if wall surfaces are not acceptable. Do not begin installation until unacceptable conditions have been corrected.

3.02 INSTALLATION

A. Install corner guards to wall securely in accordance with manufacturer’s written instructions.

B. Install corner guards accurately in location, alignment, and elevation.

C. Provide horizontal steel stud back up in drywall stud cavity to accept fasteners.

# END OF SECTION

Rev 12/17