3-Part CSI MasterFormat Specification

SECTION 10 2600

WALL AND DOOR PROTECTION

- GENERAL

## SECTION INCLUDES

### 6 inch (152.4mm) Crash Rails, Surface Mount, Economy Mount

## SUBMITTALS

### Comply with requirements of Section 01 33 00 Submittals.

### Product data: Submit manufacturer’s product data.

### Shop drawing: Submit shop drawings showing components, dimensions, anchorage details.

### Samples: Submit for approval 12 inch (304.8mm) long sample for each model and color specified, including end caps and corner units.

### Test reports: Submit manufacturer’s test reports and certification indicating compliance with applicable ADA and building code requirements

  - QUALITY ASSURANCE

    - Comply with NFPA 101 for interior finish materials. Smoke developed less than 450 and flame spread of 25 or less in accordance with ASTM E84.

  - DELIVERY, STORAGE AND HANDLING

### Delivery: Deliver materials to site in manufacturer’s original, unopened containers and packaging with labels clearly indicating manufacturer and material.

### Storage: Store materials indoors in a clean, dry area protected from damage and in accordance with manufacturer’s instructions.

### Handling: Protect materials during handling and installation to prevent damage

- - PRODUCTS

2.01 	MANUFACTURER

Nystrom

9300 73rd Ave N

Minneapolis, MN 55428

PH: 800.547.2635

www.nystrom.com

2.02 	CRASH RAIL, Economy Surface Mount, 6 inch High

- Nystrom model CRVS6E crash rail mounted over aluminum economy clips. Exposed surfaces shall be free of wrinkling, chipping, discoloration, or other imperfections.

  - Dimensions

    - Height: 6 inch (152.4mm)

    - Width: 1 inch (25.4mm).

    - Mounts flush with wall using economy retainer clips spaced 16 inch on center.

  - Profile: High impact vinyl acrylic extrusion locked into place, nominal 0.078 inch (1.98mm) thick. Class A fire rating, tested in accordance with ASTM E 84.

  - Extrusion: Pebble grain finish. Contains EPA registered Micro-Chek antimicrobial agent.

  - Retainer Clips: Nominal 2 inch (50.8mm) wide by 0.062 inch (1.57mm) thick 6063-T5 aluminum.

  - End Caps: Wall return unit of color and texture similar to that of the rail.

    - Foam cushion, Solid one-piece foam cushion.

    - Rigid plastic, Injection molded preassembled.

  - Corners: External corner units of similar material to end cap units. Carry line of crash rail continuously around corner, unless otherwise indicated on drawings.

  - Color: To be selected from manufacture’s standard colors.

EXECUTION

3.01 EXAMINATION

- Verify by examination that wall surface is acceptable to receive the specified bumper guard. Notify the Architect in writing if wall surfaces are not acceptable. Do not begin installation until unacceptable conditions have been corrected.

3.02 INSTALLATION

A. Install crash rails to wall securely in accordance with manufacturer’s written instructions.

B. Install crash rails accurately in location, alignment, and elevation.

C. Provide horizontal steel stud back up in drywall stud cavity to accept fasteners.

# END OF SECTION

Rev 12/17