3-Part CSI MasterFormat Specification

SECTION 10 2600

WALL AND DOOR PROTECTION

- - GENERAL

## SECTION INCLUDES

### 4 inch (101.6mm) Crash Rails, Aluminum Bar, Extended Mount

### 4 inch (101.6mm) Crash Rails, Stainless Steel Bar, Extended Mount

## REFERENCES

### American Society for Testing and Material (ASTM). ASTM A 276 Standard for stainless steel and heat resisting steel bars and shapes

### American Society for Testing and Material (ASTM). ASTM B 221 Standard specification for aluminum and aluminum-alloy extruded bars, rods, wire, shapes and tubes.

### Aluminum Association (AA).

## SUBMITTALS

### Comply with requirements of Section 01 33 00 Submittals.

### Product data: Submit manufacturer’s product data.

### Shop drawing: Submit shop drawings showing components, dimensions, anchorage details.

### Samples for selection and verification of product pattern and finish.

## QUALITY ASSURANCE

    - Manufacturer: A firm regularly engaged in the manufacturing of wall protection system components similar to those specified.

    - Installer: Engage a skilled installer with no less than three (3) years of documented experience installing similar types of products to the extent and complexity of those required for the project.

    - Code Compliance: Provide product that conforms to the necessary requirements of all applicable codes.

    - Single source responsibility: Provide all product systems components from a single source.

## DELIVERY, STORAGE AND HANDLING

### Delivery: Deliver materials to site in manufacturer’s original, unopened containers and packaging with labels clearly indicating manufacturer and material.

### Storage: Store materials indoors in a clean, dry area protected from damage where temperature and humidity remain stable and within 40 degree F (4 degree C) to 100 degree F (38 degree C). Materials must be stored flat.

### Handling: Protect materials during handling and installation to prevent damage

## PROJECT CONDITIONS

### Environmental conditions: Do NOT install wall surface protection systems until the installation area is enclosed and weatherproof, and until the ambient temperature within the building is maintained at not less than 70 degree F (21 degree C) for not less than 72 hours prior to installation.

- Installation locations must be enclosed, weatherproofed, and climate controlled prior to commencing installation.

## WARRANTY

### Submit supplier’s written warranty against defects in material and workmanship.

- - PRODUCTS

2.01 	MANUFACTURER

Nystrom

9300 73rd Ave N

Minneapolis, MN 55428

PH: 800.547.2635

www.nystrom.com

2.02 	CRASH RAIL, Aluminum, 4 inch High, Extended Mount

- Nystrom model CRAE4 aluminum bar crash rail mounted on standoff mounting brackets.

  - Dimensions

    - Height: 4 inch (101.6mm)

    - Thickness: 1/4 inch (6mm).

    - Mounting Bracket Stand-Offs

      - –BS: 	Square bracket 2-3/4 inch (69.85mm)

      - –B12:	I –Beam bracket 2 inch (50.8mm)

      - –B13:	I –Beam bracket 3 inch (76.2mm)

  - Profile Face: Flat Bar

  - Material: 6063-T5 Aluminum, clear anodized finish

  - End Caps: Material similar to that of the rail.

  - Corners: Internal and external corner units of similar material to end cap units. Carry line of crash rail continuously around corner, unless otherwise indicated on drawings.

2.03 	CRASH RAIL, Stainless Steel, 4 inch High, Extended Mount

- Nystrom model CRSE4 stainless steel bar crash rail with extended standoff mounting bracket.

  - Dimensions

    - Height: 4 inch (101.6mm)

    - Thickness: 1/4 inch (6mm).

    - Mounting Bracket Stand-Offs

      - –BS: 	Square bracket 2-3/4 inch (69.85mm)

      - –B12:	I –Beam bracket 2 inch (50.8mm)

      - –B13:	I –Beam bracket 3 inch (76.2mm)

  - Profile Face: Flat Bar

  - Material: Type 304 stainless steel, 16 gauge, #4 satin finish

  - Mounting Bracket Material: Aluminum 6063-T5, clear anodized

  - End Caps: Material similar to that of the rail.

  - Corners: Internal and external corner units of similar material to end cap units. Carry line of crash rail continuously around corner, unless otherwise indicated on drawings.

- - EXECUTION

3.01 EXAMINATION

- Examine the substrates and conditions under which the work is to be performed, and notify the Contractor in writing of conditions detrimental to the proper and timely completion of the work. Do not proceed with the installation until unsatisfactory conditions have been corrected.

3.02 PREPARATION

- Surface preparation: Prior to installation, clean surface to remove dirt, debris and loose particles. Perform additional preparation procedures as required per the manufacturer’s instructions.

3.03 INSTALLATION

A. Install the work of this section in strict accordance with manufacture’s written instructions.

3.04 CLEAN UP COMPLETION

A. Upon completion of the work, remove excess materials, debris and rubbish resulting from the installation and leave the area in a clean and orderly condition.

# END OF SECTION

Rev 12/17