Overview

Watertight floor door products are designed and built and used in well hatch applications. The following are general instructions for installing, operating and maintaining these floor door products. Watertight floor doors are tested to a 10ft column of water, 625psf live load. Continuous cover gasket and exterior pressure locks ensure its watertight performance.

These are recommended general guidelines only. Locally accepted installation, mounting, and sealing procedures should be followed to ensure the ultimate weather-ability and structural integrity of the floor doors installed into various types of flooring systems.

Storage Prior to Installation

Do not store floor door outside. If storage is required, ensure the floor doors properly covered and stored indoors.

- Special care is required when handling and installing floor doors. Please make sure that all framework and doors are supported during transport and installation to insure against bending or racking of the floor door.

Installation

Anchored installation

Tools Needed

drill (Bit size will vary with type of anchor)

fasteners (by others)

Gasketing or silicone caulk

The Floor Doors are built for water-tight access; proper installation is necessary to create the watertight seal between the Floor Door and mounting surface

- Watertight floor doors are designed to be surface mounted. The frame mounting holes are drilled by the contractor in the field. The mounting hardware and under gasket seals are provided by the contractor.

- Drill clearance holes through the aluminum frame flange that are appropriately sized according to the bolts or concrete anchors used. (ie. 5/16 inch, 3/8 inch or 1/2 inch, or other as field conditions require.) Mounting hardware is not provided by manufacturer. Figure 1

- Position floor door over opening and mark where fastener holes are located on the mounting surface. Prepare concrete as required.

- Secure gasketing to bottom of frame (gasket must be continuous). IF you choose to seal with silicone caulk, this step may be skipped.

- Fasten Frame to the concrete.

- If gasketing was not used, caulk the entire frame perimeter with silicone.

Operation

Floor doors are designed and built for years of dependable access. All floor doors come standard with stainless steel hardware components. The basic components for door operation include turn handle latches, and stainless steel hinges and a locking hold open arm as detailed:

- Pressure locks latches with wing nuts

- Heavy duty butt hinges

- Hold Open Arm automatically engages and locks when the door fully opens. The hold open arm must be engaged in the locked position to ensure that the door does not close unintentionally. Pull the red vinyl grip handle to unlock and safely close the door.

To open the floor door cover, unscrew the wing nuts from pressure lock latch until there is sufficient clearance for the latch to rotate down away from the cover catch. Repeat this process for all pressure lock latches located around the entire perimeter of the floor door.

Fully open the door until the hold open arm engages to lock the cover in the 90 degree open position.

To close the floor door cover, pull the red grip handle forward to disengage and gently lower the cover.

Re-install each pressure lock latch by rotating back into position and screwing wing nut to secure door in position. Final tighten all wing nuts to ensure watertight seal.

Maintenance

- Floor doors should be manually operated once a year to check performance.

- Lubricate moving parts such as hinges and latches with a silicone spray lube as required to maintain a smooth opening and closing of the door. Do not over grease. Do not use regular lubricating oil as it can attract dust and grit.

- Non-moving parts can be cleaned with a mild soap or dishwashing detergent and water solution.

- Gaskets can be cleaned with a clean, damp, lint-free cloth. Do not apply mineral oils, vinyl dressings, or other lubricants to the gasket as they can cause the gasket to break down over time.

- If any questions arise during the operation or maintenance of the products, please feel free to call toll-free number for assistance, 1-800-547-2635.

Follow the maintenance instructions to ensure the long life of the product. Contact Nystrom for information on replacing damaged parts.

# Text boxes

Model(s): FDWTA

Gasket seal/caulk under frame flange, provided by others in the field.

Frame mounting holes are drilled in the field. Spacing shown here for reference.