3-Part CSI MasterFormat Specification

SECTION 10 2600

WALL AND DOOR PROTECTION

1 GENERAL

1.1 SECTION INCLUDES

A. Handrail Systems.

1.2 RELATED SECTIONS

A. Section 06100 - Rough Carpentry: For wood blocking backup in gypsum wallboard partitions.

B. Section 09250 - Gypsum Wallboard: For light gauge metal framing and backup.

1.3 REFERENCES

A. Forest Stewardship Council.

B. Aluminum Association (AA).

C. American Society for Testing and Materials (ASTM)

1. ASTM B 221-93 Standard Specification for Aluminum and Aluminum-Alloy Extruded Bars, Rods, Wire, Shapes, and Tubes.

D. Title III of "The Americans with Disabilities Act" 1990 (ADA), Department of Justice.

1.4 SYSTEM DESCRIPTION

A. Performance Requirements (High impact vinyl handrail, bumper guard, crash rail, and corner guard systems)

1. Fire Performance Characteristics

a. Provide wall protection system components which have been determined to be self-extinguishing in accordance with ASTM D 635.

b. Provide wall protection system components which are identical to those tested in accordance with ASTM E 84, NFPA 255, and UL 723 for the fire performance characteristics specified herein (Flame Spread: 25 or less, Smoke Developed: 450 or less).

2. Impact Resistance: Provide wall protection system with a minimum impact resistance of 1.2 inch-pounds per 0.001 inch of thickness when tested in accordance with ASTM D4226.

3. Color Variation: Total color difference (Delta E) between sample and standard shall be no greater than 1.0 units using the Hunter (Lab) scale.

1.5 SUBMITTALS

A. Submit the following in accordance with Section 01300:

1. Product Data: Manufacturers product specifications, installation and maintenance instructions.

2. Shop Drawings: Show locations, extent, and installation details of each system including method of attachment and adjacent construction.

3. Samples for Selection Purposes: Actual sections of components are available in a convenient but representative size showing full range of colors, textures, and patterns for each type of wall protection system specified.

4. Samples for Verification Purposes

a. Not less than 12 inch (300mm) length of each system component including corners and end caps in selected colors, textures and patterns.

5. Maintenance Instructions: Manufacturers instructions for maintenance of installed work.

1.6 QUALITY ASSURANCE

A. Single Source Responsibility: Furnish all wall protection system components from a single source.

B. Manufacturer: A firm regularly engaged in the manufacture of wall protection system components similar to those specified.

C. Installer: A firm with at least 3 years of successful experience in the installation of wall protection systems similar to those specified.

1.7 DELIVERY, STORAGE AND HANDLING

A. Deliver materials in manufacturers packages properly labeled for identification and for location in the Project. Comply with manufacturer’s instructions for storage and handling. Damaged and otherwise unsuitable material, when so determined, shall be immediately removed from the Project site.

1.8 PROJECT CONDITIONS

A. Environmental Conditions: Do NOT install wall surface protection systems until the installation area is enclosed and weatherproof, and until the ambient temperature within the building is maintained at not less than 70 degrees F (21 degrees C) for not less than 72 hours prior to installation.

1.9 EXTRA MATERIALS

A. Furnish Owner at least 2 percent of each type, color and pattern of wall surface protection components used on the Project over and above the amount installed.

B. Deliver to Owner at time of final inspection of work under this Section and store where directed in the building.

2 PRODUCTS

2.1 ACCEPTABLE MANUFACTURERS

- Nystrom

9300 73rd Ave N

Minneapolis, MN 55428

PH: 800.547.2635

www.Nystrom.com

B. Other manufacturers seeking approval of their products must comply with requirements of the Instructions to Bidders prior to bidding.

2.2 WALL SURFACE AND CORNER PROTECTION SYSTEMS

A. Item 5 - Wallwear Wall Protection Systems - Handrail, Model WHRC-625 Round grip wood handrail with vinyl acrylic crash rail and accent strip, 6-1/4 inch (158.7mm) high

2.3 MATERIALS

A. Item 6 Material: Forest Stewardship Council (FCS) Certified, kiln-dried select or better Oak, Maple or Ash

1. Handrail: Forest Stewardship Council (FCS) Certified, kiln-dried select or better wood

a. Wood Type/Color: Ash Manufacturer's Standards

2. Snap-On Covers: Chemical and stain resistant, vinyl acrylic cover in longest lengths practicable for each system.

a. Cover Thickness: .078 inch (1.98mm)

3. Crashrail Color: Moonlight 09

4. Accent Strip Color: Moonlight 09

5. Mounting Brackets: Molded vinyl acrylic in shade to compliment wood finish

6. Fastener: 1/4 inch - 20 Bolts with type BB Toggler brand toggles by Mechanical Plastics

3 EXECUTION

3.1 EXAMINATION

A. Examine the substrates and conditions under which the work is to be performed, and notify the Contractor in writing of conditions detrimental to the proper and timely completion of the work. Do not proceed with the installation until unsatisfactory conditions have been corrected.

B. Ensure that surfaces to receive materials specified are properly prepared.

3.2 INSTALLATION

A. Install products in accordance with manufacturer’s instructions, at locations shown.

B. Where applicable, install systems to comply with ADA Article 4.26.

# END OF SECTION

Rev 12/17