3-Part CSI MasterFormat Specification

SECTION 10 2600

WALL AND DOOR PROTECTION

- - GENERAL

## SECTION INCLUDES

### Corner Guard, Stainless Steel

- Corner Guard End Wall, Stainless Steel

## SUBMITTALS

### Comply with requirements of Section 01 33 00 Submittals.

### Product data: Submit manufacturer’s product data.

### Shop drawing: Submit shop drawings showing components, dimensions, anchorage details.

### Samples: Submit for approval 12 inch (304.8mm) long sample for each model and color specified, including end caps and corner units.

  - QUALITY ASSURANCE

### Single Source Responsibility: Furnish all wall protection system components from a single source.

### Manufacturer: A firm regularly engaged in the manufacture of wall protection system components similar to those specified.

### Installer: A firm with at least 3 years of successful experience in the installation of wall protection systems similar to those specified.

  - DELIVERY, STORAGE AND HANDLING

### Delivery: Deliver materials to site in manufacturer’s original, unopened containers and packaging with labels clearly indicating manufacturer and material.

### Storage: Store materials indoors in a clean, dry area protected from damage and in accordance with manufacturer’s instructions.

### Handling: Protect materials during handling and installation to prevent damage

- - PRODUCTS

2.01 	MANUFACTURER

Nystrom

9300 73rd Ave N

Minneapolis, MN 55428

PH: 800.547.2635

www.nystrom.com

2.02 	CORNER GUARD, STAINLESS STEEL, SURFACE MOUNT

- Nystrom model CGSS Surface mount stainless steel corner guard with variable wings

  - Dimensions

    - Wing size: 1 inch minimum to customer specified maximum

    - Corner angle type: 90 degree standard

      - Specify other (135 degree)

  - Material (Specifier to choose one and delete the other)

    - Stainless Steel Type #304, 16 Gauge Stainless Steel, Satin #4 Finish with rounded edged and protective coating

      - Contact manufacturer for finish options

    - Stainless Steel Type #430, 16 Gauge Stainless Steel, Satin #4 Finish with rounded edged and protective coating

  - Mounting: (Specifier to choose one and delete the other)

    - Mastic Adhesive

    - Mechanically fastened with screws

- Nystrom model CGSS-EW Surface mount stainless steel end wall with variable wings and inside dimensions

  - Dimensions

    - Wing size: 1 inch minimum to customer specified maximum

    - Inside Dimension: customer specified width

    - Corner angle type: 90 degree standard

      - Specify other (135 degree)

  - Material (Specifier to choose one and delete the other)

    - Stainless Steel Type #304, 16 Gauge Stainless Steel, Satin #4 Finish with rounded edged and protective coating

      - Contact manufacturer for finish options

    - Stainless Steel Type #430, 16 gauge Stainless Steel, Satin #4 Finish with rounded edged and protective coating

  - Mounting: (Specifier to choose one and delete the other)

    - Mastic Adhesive

    - Mechanically fastened with screws

- Nystrom Model CGSR2SD Flush mount, stainless steel corner guard with 2 inch wings.

  - Dimensions

    - Wing size: 2 inch

    - Corner Angle type: 90 degree

  - Material

    - Stainless Steel Type #304, 16 gauge Stainless Steel, Satin #4 Finish with rounded edged and protective coating

    - Stainless Steel Type #430, 16 gauge Stainless Steel, Satin #4 Finish with rounded edged and protective coating

  - Mounting:

    - Mechanically fastened with screws

- Nystrom Model CGSR3SD Flush mount stainless steel corner guard with 3 inch wings.

  - Dimensions

    - Wing size: 3 inch

    - Corner Angle type: 90 degree

  - Material

    - Stainless Steel Type #304, 16 gauge Stainless Steel, Satin #4 Finish with rounded edged and protective coating

    - Stainless Steel Type #430, 16 gauge Stainless Steel, Satin #4 Finish with rounded edged and protective coating

  - Mounting:

    - Mechanically fastened with screws

- - EXECUTION

3.01 EXAMINATION

- Verify by examination that wall surface is acceptable to receive the specified bumper guard. Notify the Architect in writing if wall surfaces are not acceptable. Do not begin installation until unacceptable conditions have been corrected.

3.02 INSTALLATION

A. Install corner guards to wall securely in accordance with manufacturer’s written instructions.

B. Install corner guards accurately in location, alignment, and elevation.

C. Provide horizontal steel stud back up in drywall stud cavity to accept fasteners.

# END OF SECTION

Rev 12/17