3-Part CSI MasterFormat Specification

SECTION 10 2600

WALL AND DOOR PROTECTION

- - GENERAL

## SECTION INCLUDES

### 5-1/2 inch (139.7mm) Hand Rail, Vinyl

### 5-1/2 inch (139.7mm) Hand Rail, Vinyl, 2 inch Accent Strip

### 5-1/2 inch (139.7mm) Hand Rail, Vinyl, Thumb Grip

## SUBMITTALS

### Comply with requirements of Section 01 33 00 Submittals.

### Product data: Submit manufacturer’s product data.

### Shop drawing: Submit shop drawings showing components, dimensions, anchorage details.

### Samples: Submit for approval 12 inch (304.8mm) long sample for each model and color specified, including end caps and corner units.

### Test reports: Submit manufacturer’s test reports and certification indicating compliance with applicable ADA and building code requirements

  - QUALITY ASSURANCE

    - Comply with NFPA 101 for interior finish materials. Smoke developed less than 450 and flame spread of 25 or less in accordance with ASTM E84.

  - DELIVERY, STORAGE AND HANDLING

### Delivery: Deliver materials to site in manufacturer’s original, unopened containers and packaging with labels clearly indicating manufacturer and material.

### Storage: Store materials indoors in a clean, dry area protected from damage and in accordance with manufacturer’s instructions.

### Handling: Protect materials during handling and installation to prevent damage

- - PRODUCTS

2.01 	MANUFACTURER

Nystrom

9300 73rd Ave N

Minneapolis, MN 55428

PH: 800.547.2635

www.Nystrom.com

2.02 	HAND RAIL, Vinyl, 5-1/2 inch

- Nystrom model HRVE55C hand rail mounted over continuous aluminum retainer and full length vinyl bumper cushion with mounting brackets maintaining wall clearance. Exposed surfaces shall be free of wrinkling, chipping, discoloration, or other imperfections.

  - Dimensions

    - Height: 5-1/2 inch (139.7mm)

    - Width: 1-1/2 inch (38.1mm)

    - Clearance from Wall: 1-1/2 inch (38.1mm) Bracket

  - Profile: Oval, high impact vinyl acrylic extrusion locked into place, nominal 0.078 inch (1.98mm) thick. Class A fire rating, tested in accordance with ASTM E 84.

  - Extrusion: Pebble grain finish. Contains EPA registered Micro-Chek antimicrobial agent.

  - Retainer: Continuous 6063-T5 aluminum retainer along entire length of handrail bumper, nominal 0.080 inch (2.03mm) thick.

  - End Caps: Rigid plastic wall return unit of color and texture similar to that of rail.

  - Corners: Internal and external corner units of similar material to end cap units. Carry line of hand rail continuously around corner, unless otherwise indicated on drawings.

  - Optional Reveal: Black 1/8 inch (3.2mm) wide flexible insert between profile cover and end cap/corner provides aesthetic design.

  - Color: To be selected from manufacture’s standard colors.

2.03 	HAND RAIL, Vinyl, 5-1/2 inch, with 2 inch Accent Strip

- Nystrom model HRVE55C-AS hand rail with accent strip mounted over continuous aluminum retainer and full length vinyl bumper cushion with mounting brackets maintaining wall clearance. Exposed surfaces shall be free of wrinkling, chipping, discoloration, or other imperfections.

  - Dimensions

    - Height: 5-1/2 inch (139.7mm)

    - Width: 1-1/2 inch (38.1mm)

    - Clearance from Wall: 1-1/2 inch (38.1mm) Bracket

  - Profile: Oval with 2 inch (50.8mm) accent strip, high impact vinyl acrylic extrusion locked into place, nominal 0.078 inch (1.98mm) thick. Class A fire rating, tested in accordance with ASTM E 84.

  - Extrusion: Pebble grain finish. Contains EPA registered Micro-Chek antimicrobial agent.

  - Retainer: Continuous 6063-T5 aluminum retainer along entire length of handrail bumper, nominal 0.080 inch (2.03mm) thick.

  - End Caps: Rigid plastic wall return unit of color and texture similar to that of rail.

  - Corners: Internal and external corner units of similar material to end cap units. Carry line of hand rail continuously around corner, unless otherwise indicated on drawings.

  - Optional Reveal: Black 1/8 inch (3.2mm) wide flexible insert between profile cover and end cap/corner provides aesthetic design.

  - Color: To be selected from manufacture’s standard colors.

2.04 	HAND RAIL, Vinyl, 5-1/2 inch, with Thumb Grip

- Nystrom model HRVE55C-TG hand rail mounted over continuous aluminum retainer and full length vinyl bumper cushion with mounting brackets maintaining wall clearance. Exposed surfaces shall be free of wrinkling, chipping, discoloration, or other imperfections.

  - Dimensions

    - Height: 5-1/2 inch (139.7mm)

    - Width: 1-1/2 inch (38.1mm)

    - Clearance from Wall: 1-1/2 inch (38.1mm) Bracket

  - Profile: Oval with thumb grip, high impact vinyl acrylic extrusion locked into place, nominal 0.078 inch (1.98mm) thick. Class A fire rating, tested in accordance with ASTM E 84.

  - Extrusion: Pebble grain finish. Contains EPA registered Micro-Chek antimicrobial agent.

  - Retainer: Continuous 6063-T5 aluminum retainer along entire length of handrail bumper, nominal 0.080 inch (2.03mm) thick.

  - End Caps: Rigid Plastic wall return unit of color and texture similar to that of rail.

  - Corners: Internal and external corner units of similar material to end cap units. Carry line of hand rail continuously around corner, unless otherwise indicated on drawings.

  - Optional Reveal: Black 1/8 inch (3.2mm) wide flexible insert between profile cover and end cap/corner provides aesthetic design.

  - Color: To be selected from manufacture’s standard colors.

- EXECUTION

3.01 EXAMINATION

- Verify by examination that wall surface is acceptable to receive the specified bumper guard. Notify the Architect in writing if wall surfaces are not acceptable. Do not begin installation until unacceptable conditions have been corrected.

3.02 INSTALLATION

A. Install hand rails to wall securely in accordance with manufacturer’s written instructions.

B. Install hand rails accurately in location, alignment, and elevation.

C. Provide horizontal steel stud back up in drywall stud cavity to accept fasteners.

# END OF SECTION

Rev 12/17