3-Part CSI MasterFormat Specification

SECTION 10 2600

WALL AND DOOR PROTECTION

- - GENERAL

## SECTION INCLUDES

### 2-11/16 inch (68.3mm) by 2-11/16 inch (68.3mm) Door Frame Guard, Vinyl, 2-11/16 inch, Bull Nose

## SUBMITTALS

### Comply with requirements of Section 01 33 00 Submittals.

### Product data: Submit manufacturer’s product data.

### Shop drawing: Submit shop drawings showing components, dimensions, anchorage details.

### Samples: Submit for approval 12 inch (304.8mm) long sample for each model and color specified, including end caps and corner units.

### Test reports: Submit manufacturer’s test reports and certification indicating compliance with applicable ADA and building code requirements

  - QUALITY ASSURANCE

    - Comply with NFPA 101 for interior finish materials. Smoke developed less than 450 degree F and flame spread of 25 or less in accordance with ASTM E84.

  - DELIVERY, STORAGE AND HANDLING

### Delivery: Deliver materials to site in manufacturer’s original, unopened containers and packaging with labels clearly indicating manufacturer and material.

### Storage: Store materials indoors in a clean, dry area protected from damage and in accordance with manufacturer’s instructions.

### Handling: Protect materials during handling and installation to prevent damage.

- - PRODUCTS

2.01 	MANUFACTURER

Nystrom

9300 73rd Ave N

Minneapolis, MN 55428

PH: 800.547.2635

www.Nystrom.com

2.02 	DOOR FRAME GUARD, Vinyl, 2-11/16 inch, Bull Nose

- Nystrom model DGV26875 corner guard mounted on continuous aluminum retainer. Exposed surfaces shall be free of wrinkling, chipping, discoloration, or other imperfections.

  - Dimensions

    - Wing size: 2-11/16 inch (68.3mm)

    - Corner angle type: 90 degree, Bull nose 1-1/4 inch radius

  - Profile: High impact vinyl acrylic extrusion locked into place, nominal 0.100 inch (2.54mm) thick. Class A fire rating, tested in accordance with ASTM E 84.

  - Extrusion: Pebble grain finish. Contains EPA registered Micro-Chek antimicrobial agent.

  - Retainer: Continuous 6063-T5 aluminum retainer behind entire height of door frame guard, nominal 0.060 inch (1.52mm) thick.

  - End Caps: Injection molded preassembled wall return unit of color and texture similar to that of the corner guard.

  - Color: To be selected from manufacture’s standard colors.

- - EXECUTION

3.01 EXAMINATION

- Verify by examination that wall surface is acceptable to receive the specified bumper guard. Notify the Architect in writing if wall surfaces are not acceptable. Do not begin installation until unacceptable conditions have been corrected.

3.02 INSTALLATION

A. Install door frame guard to frame securely in accordance with manufacturer’s written instructions.

B. Install door frame guard accurately in location, alignment, and elevation.

# END OF SECTION

Rev 12/17