SECTIONS 05.51.00, 07.72.20, 08.31.00

SAFETY POST FOR FIXED VERTICAL LADDERS USED WITH ROOF HATCHES AND FLOOR DOORS

GENERAL

SUMMARY

Section includes: Furnishing and installing safety post for fixed ladders in roof hatches and floor doors.

Related Sections:  [Insert applicable specifications sections]

references

American Society for Testing and Materials (ASTM)

ASTM A 36-93a: Standard Specification for Structural Steel

SUBMITTALS

Shop Drawings: Show profiles, hardware, accessories, location and dimensions.

Samples: Manufacturer to provide upon request, size to represent material adequately.

Manufacturer's Installation Instructions:  Indicate installation requirements.

DELIVERY, STORAGE, and HANDLING

Deliver materials to Project site ready use.

Exercise proper care in handling of Work so as not to disrupt finished surfaces.

Store materials under cover in a dry and clean location off the ground.

job conditions and sequencing

Coordinate with other trades any related work to avoid delay.

Provide inserts and anchoring devices that will be built into other Work for installation of Safety Post.

Observe all appropriate OSHA safety guidelines for this work.

WARRANTY

Provide manufacturer's standard warranty.  All safety posts shall be free from manufacturing defects in materials and workmanship for a period of five (5) years from the date of shipment.  Should a product fail to function in normal use within this period, manufacturer shall furnish a new part at no charge

PRODUCTS

MANUFACTURER

Nystrom Inc

9300 73rd Ave N Brooklyn Park, MN  55428

Toll Free Hotline: 800-547-2635	Direct Phone: 763-488-9200

Toll Free Fax: 800-317-8770		Direct Fax: 763-488-9201

E-Mail:  support@nystrom.com	Internet:  www.nystrom.com

SAFETY POST FOR FIXED LADDERS

Safety Post, Steel, Yellow Powder Coat

Performance Requirements: Fabricate safety post to comply with OSHA 1910.27 for fixed ladders.  Must support 200 pound load.

Post:  1 1/2” x 1 1/2” Steel square tubing- high strength. A pull up loop shall be provided at the upper end of the post to facilitate raising the post.

Finish:  Powder coat paint, Safety Yellow.

Spring assist: Stainless steel balancing spring mechanism shall be provided to provide smooth, easy, controlled operation when raising and lowering the safety post.

Hardware: All mounting hardware shall be stainless steel.

Acceptable Product Model: SPY

Safety Post, Steel, Hot Dip Galvanized

Performance Requirements: Fabricate safety post to comply with OSHA 1910.27 for fixed ladders.  Must support 200 pound load.

Post:  1 1/2” x 1 1/2” Steel square tubing- high strength. A pull up loop shall be provided at the upper end of the post to facilitate raising the post.

Finish:  Hot Dip Galvanized

Spring assist: Stainless steel balancing spring mechanism shall be provided to provide smooth, easy, controlled operation when raising and lowering the safety post.

Hardware: All mounting hardware shall be stainless steel.

Acceptable Product Model: SPG

Safety Post, Steel, Aluminum

Performance Requirements: Fabricate safety post to comply with OSHA 1910.27 for fixed ladders.  Must support 200 pound load.

Post:  1 1/2” x 1 1/2” Steel square tubing- high strength. A pull up loop shall be provided at the upper end of the post to facilitate raising the post.

Finish:  Hot Dip Galvanized

Spring assist: Stainless steel balancing spring mechanism shall be provided to provide smooth, easy, controlled operation when raising and lowering the safety post.

Hardware: All mounting hardware shall be stainless steel.

Acceptable Product Model: SPA

Safety Post, Stainless Steel Type 304

Performance Requirements: Fabricate safety post to comply with OSHA 1910.27 for fixed ladders.  Must support 200 pound load.

Post:  1 1/2” x 1 1/2” Steel square tubing- high strength. A pull up loop shall be provided at the upper end of the post to facilitate raising the post.

Finish:  Hot Dip Galvanized

Spring assist: Stainless steel balancing spring mechanism shall be provided to provide smooth, easy, controlled operation when raising and lowering the safety post.

Hardware: All mounting hardware shall be stainless steel.

Acceptable Product Model: SPS

EXECUTION

EXAMINATION

Verify that preparation and affected dimensions are acceptable and will not disrupt other trades.

Verify that the ladder rungs are dry, clean and free of foreign matter..

Verify tolerances and correct improper conditions.

PREPARATION

Advise installers of details relating to safety post locations of supports, and anchoring methods.

INSTALLATION

Follow manufacturer’s instructions for installing safety post.

The manufacturer shall furnish fasteners necessary for installing ladder safety post on ladder rungs, reinforcing if hollow.  Secure rigidly in place.

CLEAN AND ADJUST

Clean adjacent surfaces and remove unused product and debris from site.

END OF SECTION

SECTION 05.51.00, 07.72.00, 08.31.00