3-Part CSI MasterFormat Specification

SECTION 07 72 33 or SECTION 05 52 13

Roof Accessories:  safety railings

Rev 08/23

- GENERAL

      - SUMMARY

        - Section includes:

          - Accessory Products for Roof Top Products

            - Safety Railings

      - REFERENCES

        - Division 05 for ladders and stairs

        - Division 07 for roofing and sealants

      - ACTION SUBMITTALS

        - Shop Drawings:  Indicate configuration and dimension of components, adjacent construction, required clearances and tolerances, and other affected Work.

          - General:  Show connections of units and hardware to other Work.  Include schedules showing location of each type and size of unit.

        - Product Data:  Manufacturer’s technical data for each type of hatch assembly, including setting drawings, templates, finish requirements, and details of anchorage devices.

      - INFORMATIONAL SUBMITTALS

        - Provide manufacturer's standard 5-year warranty.  All safety railings shall be free from manufacturing defects in materials and workmanship for a period of five (5) years from the date of shipment.  Should a product fail to function in normal use within this period, manufacturer shall furnish a replacement or new part at manufacturers’ discretion.

        - Sustainable Design Submittals: Building Product Disclosure Requirements: To encourage the use of building products that are working to minimize their environmental and health impacts, provide the following information when available:

          - Material Ingredients Documentation demonstrating the chemical inventory of the product

      - CLOSEOUT SUBMITTALS

        - Installation, Operating & Maintenance manuals

      - QUALITY ASSURANCE

        - Qualifications:

          - Manufacturer/Installer:  Company specializing in manufacturing and installation of components specified in this Section with minimum of 5 years documented experience.

      - DELIVERY, STORAGE, AND HANDLING

        - Deliver materials to Project site ready use.

        - Exercise proper care in handling of Work so as not to disrupt finished surfaces.

        - Store materials under cover in a dry and clean location off the ground.

- PRODUCTS

      - MANUFACTURER

        - Nystrom

9300 73rd Ave N.

Minneapolis, MN  55428

PH: 800-547-2635

www.nystrom.com

      - SAFETY RAILINGS

        - Safety Railing System: Model SRC Roof-hatch manufacturer's standard system including rails, clamps, fasteners, safety barrier at railing opening, and accessories required for a complete installation; attached to roof hatch and complying with OSHA 29 CFR 1910.29 &  CFR 1910.28 . requirements and authorities having jurisdiction.

          - Height: 42 inches (1060 mm) above finished roof deck.

          - Rails:

            - Aluminum pipe, 1-1/4 inch (31 mm), 1.66 inch (42 mm) outside diameter, schedule 40 6061 T6 alloy pipe.

            - Fittings: Cast aluminum 5052-H32 alloy with set screw hold.

            - Mounting Brackets: 3/16 inch (4.75 mm) steel, zinc plated with nut backing plate.

            - Exit: [Self-closing gate, 1-1/4 inch (32 mm) aluminum self-closing with coil spring] [Chain, 3/16 inch (4.76 mm) zinc plated steel link chain with spring clip ends].

- EXECUTION

      - ADJUSTING

        - Adjust movable parts for smooth operation.

        - Operational Units:  Test-operate units with operable components.  Clean and lubricate joints and hardware.  Adjust for proper operation.

      - CLEANING

        - Clean exposed surfaces per manufacturer's written instructions.  Touch up damaged metal coatings.

END OF SECTION