SECTION 07 72 00

Safety Railings for Roof Hatches, Floor Doors, Smoke Vents

3-Part Specification

- GENERAL

      - Summary

        - Section includes:

          - Safety railings for roof hatches installed to counterflashing.  Included related hardware.

        - Related Sections:

          - Division 5 - Metal Fabrications.

          - Division 7 – Roof Accessories.

          - Division 7 - Joint Sealants.

          - Division 9 – Paints and Coatings.

          - Division 15 – Mechanical.

      - Submittals

        - Shop Drawings:  Indicate configuration and dimension of components, adjacent construction, required clearances and tolerances, and other affected Work.

          - General:  Show connections of units and hardware to other Work.  Include schedules showing location of each type and size of unit.

        - Product Data:  Manufacturer’s technical data for each type of railing assembly, including setting drawings, templates, finish requirements, and details of mounting hardware.

        - Manufacturer's Installation Instructions:  Indicate installation requirements.

        - Quality Control Submittals:

          - Statement of qualifications.

        - Contract Closeout Submittals:

          - Operating and maintenance manuals.

      - Quality Assurance

        - Qualifications:

          - Manufacturer/Installer:  Company specializing in manufacturing and installation of components specified in this Section with minimum of 5 years documented experience.

        - Regulatory Requirements:

          - OSHA Compliance:  Provide hatch safety railing system as required by OSHA Standard 1910.23 and 1910.27 and as specified in Section.

      - Delivery, Storage, and Handling

        - Exercise proper care in handling of Work so as not to injure finished surfaces.  Protect Work from damage after it is in place.

        - Store materials under cover in a dry and clean location off the ground.  Remove materials that are damaged or otherwise not suitable for installation from Project site and replace with acceptable materials at no additional cost to Owner.

      - WARRANTY

        - Provide manufacturer's written 25-year warranty for materials and workmanship against defects.

- PRODUCTS

      - Manufacturer

          - Nystrom

9300 73rd Ave. N.

Brooklyn Park, MN 55431

Toll Free Hotline: 800-547-2635

Toll Free Fax: 800-317-8770

Direct Phone: 763-488-9200

Direct Fax: 763-488-9201

Email info@nystrom.com

Internet:  www.nystrom.com

      - safety RAILINGs

        - Top rail, Mid rail and upright posts:  Galvanized Steel Pipe, 1 ¼” ID, A53 Grade B pipe.

        - Exit:  Self Closing Gate;   Galvanized Steel Pipe, 1 ¼” ID A53 Grade B pipe, U bolt with hinge attachment and galvanized mounting bolts and nut hardware.

          - Option:  Chain, link, galvanized steel

Fittings:  Manufacturer’s standard aluminum magnesium alloy, cast with set screw pipe mount.

        - Fittings:  Manufacturer’s standard aluminum magnesium alloy, cast with set screw pipe mount

        - Counterflash Mount:  CRS, zinc plated mounting bracket with backer plate, pemmed nut for easy installation.

        - Hardware:  Bolts and Tooling:  3/8 inch by 2-1/2 inch, grade Z, zinc plated, wrench for assembly

        - OSHA Compliance:  Provide hatch safety railing system as required by OSHA Standard 1910.23 and 1910.27 and as specified.

          - Top Rail Height:  42 inches +/-3” above finished roof deck.

          - Top-Mid Rail Spacing:  21” diameter maximum.

          - Meets 200lb deflection load when mounted to roof hatch counterflash.

          - Upright post maximum spacing of 8’.

        - Acceptable Product:  Safety Railing for Roof Hatch, Model Number SRCG

- EXECUTION

      - EXAMINATION

        - Verification of Conditions:  Examine areas and conditions under which Work is to be performed and identify conditions detrimental to proper or timely completion.

        - Verify that deck, curbs, roof membrane, base flashing, and other items affecting Work of this Section are in place and positioned correctly.

        - Verify tolerances and correct improper conditions.

        - Do not proceed until unsatisfactory conditions have been corrected.

      - Installation

        - Install roof accessory items and components per manufacturer's instructions.

        - Coordinate installation of components of this Section with installation of roof deck, roof structure, roofing membrane, and base flashing.

      - ADJUSTING

        - Adjust movable parts for smooth operation.

        - Operational Units:  Test-operate units with operable components, open/close gate.

      - cleaning

        - Clean exposed surfaces per manufacturer's written instructions.  Touch up damaged metal coatings.

END OF SECTION